## Slide 1: CY 2550 Foundations of Cybersecurity
(Distributed) Denial of Service

## Slide 2: Security Properties, Revisited
Confidentiality
Integrity
Authenticity
Availability
  Data and resources must be accessible when required
  Related to integrity, but more concerned with denial of service (DoS)
    Resource exhaustion (e.g., CPU, memory, network bandwidth)
    Usually easy to perform, and very difficult to defend against

## Slide 3: Ping
Essential, low-level network utility
Sends a “ping” ICMP message to a host on the internet
$ ping 66.66.0.255
PING 66.66.0.255 (66.66.0.255) 56(84) bytes of data.
64 bytes from 66.66.0.255: icmp_seq=1 ttl=58 time=41.2 ms
Destination host is supposed to respond with a “pong”
  Indicating that it can receive packets
By default, ping messages are 56 bytes long (+ some header bytes)
  Maximum size 65535 bytes
What if you send a ping that is >65535 bytes long?

## Slide 4: Ping of Death
$ ping –s 65535 66.66.0.255

## Slide 5: iOS Telegu Unicode Bug
February 2018: iPhones and iPads crash if they receive text or email containing a specific symbol in Indian
In some cases, reboot doesn’t solve the issue
  Apps reload bugged messages automatically on startup and crash again
Device wipe is sometimes the only fix

## Slide 6: Denial of Service (DoS)
Prevent a person from being able to access a specific computer, service, or piece of data
In essence, an attack on availability
Possible vectors:
  Exploit bugs that lead to crashes
  Exhaust the resources of a target
Often very easy to perform…
… and fiendishly difficult to mitigate

## Slide 7: Distributed Denial of Service

## Slide 8: Attacker Goals and Threat Model
Internet
Servers
128.91.0.*
66.66.0.11
I wanna knock those servers offline… but how?
Goal is to reduce the availability of the victim
Active attacker who may send arbitrary packets
Resource exhaustion attack, not a bug or exploit

## Slide 9: DoS Attack Parameters
Goal: exhaust the victim’s bandwidth
How much bandwidth is available to the attacker?
  Can be increased by controlling more resources…
  Or tricking others into participating in the attack
What kind of packets do you send to victim?
  Minimize effort and risk of detection for the attacker…
  While also maximizing damage to the victim

## Slide 10: Exploiting Asymmetry
Internet
Server
128.91.0.1
66.66.0.11
10 Mbps
1 Mbps
1 Mbps
10 Mbps
Example of a Distributed Denial of Service Attack (DDoS)
How to achieve scale?
  Volunteers
  Reflection and amplification
  Botnet

## Slide 11
Dumbest tool ever: doesn’t spoof your IP address
Guarantees that you will be caught by law enforcement

## Slide 12: The Smurf Attack
Internet
Server
128.91.0.1
66.66.0.11
10.7.0.0
10.7.0.1
10.7.0.253
10.7.0.254
…
PING Request
Src: 128.91.0.1
Dst: 10.7.0.255
*.*.*.255 is a broadcast packet
Forwarded to all hosts in the /24

## Slide 13: Why Does Smurfing Work?
ICMP protocol does not include authentication
  No connections
  Receivers accept messages without verifying the source
  Enables attackers to spoof the source of messages
Attacker benefits from an amplification factor
  Smurf amp factor  [number of servers that respond to the broadcast]:1

## Slide 14: Reflection/Amplification Attacks
Smurfing is an example of a reflection or amplification DDoS attack
Fraggle attack also relies on broadcasts for amplification
  Send spoofed UDP packets to IP broadcast addresses on port 7 (echo) and 13 (chargen)
    echo – 1500 bytes/pkt requests, equal size responses
    chargen – 28 bytes/pkt request, 10K-100K bytes of ASCII in response
  Amp factor
    echo  [number of hosts responding to the broadcast]:1
    chargen  [number of hosts responding to the broadcast]*360:1

## Slide 15: DNS Reflection Attack
Spoof DNS requests to many open DNS resolvers
  DNS is a UDP-based protocol, no authentication of requests
  Open resolvers accept requests from any client
    E.g. 8.8.8.8, 8.8.4.4, 1.1.1.1, 1.0.0.1
  February 2014 – 25 million open DNS resolvers on the internet
64 byte DNS queries generate large responses
  Old-school “A” record query  maximum 512 byte response
  EDNS0 extension “ANY” record query  1000-6000 byte response
    E.g. $ dig ANY isc.org
  Amp factor – 180:1
Attackers have been known to register their own domains and install very large records just to enable reflection attacks!

## Slide 16: Reflection Example
Internet
Server
128.91.0.1
DNS Request
Src: 128.91.0.1
Dst: whatever
50 Gbps
5 Gbps
100 Gbps

## Slide 17: NTP Reflection Attack
Spoof requests to open Network Time Protocol (NTP) servers
  NTP is a UDP-based protocol, no authentication of requests
  May 2014 – 2.2 million open NTP servers on the internet
234 byte queries generate large responses
  monlist query: server returns a list of all recent connections
  Other queries are possible, i.e. version and showpeers
  Amp factor – from 10:1 to 560:1

## Slide 18: memcached Reflection Attack
Spoof requests to open memcached servers
  Popular <key:value> server used to cache web objects
  memcached uses a UDP-based protocol, no authentication of requests
  February 2018 – 50k open memcached servers on the internet
1460 byte queries generate large responses
  A single query can request multiple 1MB <key:value> pairs from the database
  Amp factor – up to 50000:1

## Slide 19: Reflection Amplification
Protocol | Amplification Factor
memcached | 50000
NTP | 557
chargen | 359
DNS | 179
QOTD | 140
BitTorrent | 54
SSDP | 31
SNMPv2 | 6
Steam | 6
NetBIOS | 4

## Slide 20
Taming the 800 Pound Gorilla: The Rise and Decline of NTP DDoS Attacks – https://dl.acm.org/citation.cfm?id=2663717

## Slide 21: Infamous DDoS Attacks
When | Against Whom | Size | How
March 2013 | Spamhaus | 120 Gbps | Botnet + DNS reflection
February 2014 | Cloudflare | 400 Gbps | Botnet + NTP reflection
September 2016 | Krebs | 620 Gbps | Mirai
October 2016 | Dyn (major DNS provider) | 1.2 Tbps | Mirai
March 2018 | Github | 1.35 Tbps | Botnet + memcached refection

## Slide 22: Denial of Service as a Service

## Slide 23: Denial of Service as a Service
Booters and Stressors
Websites that claim to “test” a target for resilience against DDoS
  Send huge amounts of traffic to a target for a fee
  $10-$100 depending on the amount of traffic and duration of the “test”
Obvious front for criminal DDoS attacks
  Users can “test”, i.e. attack, any website they want for a fee
  Attack bandwidth drawn from botnets and bulletproof hosts
Many, many stressor services operating out in the open

## Slide 25
Might be bulletproof, might be a botnet

## Slide 26: Hacked & Dumped Booter Services
99.4% via Paypal
Stress Testing the Booters: Understanding and Undermining the Business of DDoS Services – https://dl.acm.org/citation.cfm?id=2883004

## Slide 27: Booter Attack Characteristics
Stress Testing the Booters: Understanding and Undermining the Business of DDoS Services – https://dl.acm.org/citation.cfm?id=2883004

## Slide 28: Amplifier Locations
Stress Testing the Booters: Understanding and Undermining the Business of DDoS Services – https://dl.acm.org/citation.cfm?id=2883004

## Slide 29: Payment Interventions
Stress Testing the Booters: Understanding and Undermining the Business of DDoS Services – https://dl.acm.org/citation.cfm?id=2883004
h
h
h
h

## Slide 30: Mitigations
Anti-amplification
Filters
Anti-spoofing
CDNs

## Slide 31: Potential Mitigations
Don’t become an amplifier, help shut down amplifiers
  If resources aren’t available to attackers, DDoS is much harder
Network filters – traffic filtering and spoofing filters
  Try to stop DDoS traffic from reaching your network
Content distribution Networks
  Leverage a hosting service with a huge amount of capacity

## Slide 32: Avoid Becoming an Amplifier
Don’t be part of the problem!
  The behavior of your software and network impacts the well-being of others
Filter ingress IP broadcasts at the gateway router
  i.e. drop anything destined to *.*.*.255
Disable non-essential services
  echo, chargen, NTP, etc.
Configure services to only respond to requests from the local LAN
  Firewall ports 53 (DNS), 123 (NTP), 11211 (memcached), etc.
If you write a UDP service, authenticate the sources of packets
  TCP is connection-oriented, and thus much less vulnerable

## Slide 33: Outreach
Researchers are trying to clean up amplifiers
  Scan for servers with open services that are possible amplifiers
  Manually contact server owners, ISPs, and ASs
  Issue public advisories
  Get vendors to issue patches that disable services or features by default

## Slide 34: Example: NTP monlist Cleanup
Exit from Hell? Reducing the Impact of Amplification DDoS Attacks – https://www.usenix.org/system/files/conference/usenixsecurity14/sec14-paper-kuhrer.pdf

## Slide 35: What About Filtering?
Web Server
Stop
Stop
Success! Some of the attack is halted
Stop
Stop
Problems:
The ingress links are still saturated
No idea where the attack is coming from
Problems:
Legitimate traffic is still blocked
How do you get Tier 1 ASs to install filters for you?

## Slide 36: Problems With Filters
Packet filtering is not a viable solution
If you install a local filter:
  Ingress links are still saturated
  Very hard to distinguish DDoS packets from legitimate requests, since sources are spoofed
Remote filters work better, but:
  You still need to track down the source of the attack
  You have no ability to force ISPs and ASs to install filters on your behalf

## Slide 37: In-Network Defenses
Why don’t ISPs/ASs drop spoofed packets?
Unicast Reverse Path Forwarding (uRPF)
  Routers validate the source IP addresses against routing tables
  “Unlikely” source addresses are dropped
uRPF modes:
  Strict – may drop legitimate traffic (false positives)
  Feasible – may accept spoofed traffic (false negatives)
  Loose – only drops unroutable sources like 192.168.*.*
Most ISPs/ASs don’t implement uRPF
  Unwilling to risk false positives from strict mode
  No incentive to implement security measures

## Slide 38: Content Delivery Networks (CDNs)
CDNs help companies scale-up their websites
  Cache customer content on many replica servers
  Users access the website via the replicas
Examples: Akamai, Cloudflare, Rackspace, Amazon Cloudfront, etc.
Side-benefit: DDoS protection
  CDNs have many servers, and a huge amount of bandwidth
  Difficult to knock all the replicas offline
  Difficult to saturate all available bandwidth
  No direct access to the master server
Cloudflare: 15 Tbps of bandwidth over 149 data centers

## Slide 39: CDN Basics
Master
Website content and database is here
Content is cached in the replicas
Users requests all go through the replicas
Most served from cache

## Slide 40: DDoS Defense via CDNs
Master
What if you DDoS the master replica?
  Cached copies in the CDN still available
  Easy to do ingress filtering at the master
What if you DDoS the replicas?
  Difficult to kill them all
  Dynamic DNS can redirect users to live replicas

## Slide 41: Techniques for IP Traceback
The IP Protocol includes a Record Route option
  If enabled by the sender (and supported by routers), each router inserts its IP into the packet payload
However, Record Route is off by default
  No attacker would ever voluntarily enable it, since it would reveal their IP
Several proposals in the research literature for lightweight, on-by default record route systems
  Practical Network Support for IP Traceback [Savage00]
  Pi: A Path Identification Mechanism to Defend against DDoS Attacks [Yaar03]
These systems would be great, but require all Internet routers to be upgraded :(

## Slide 42: Standard DDoS, Revisited
Internet
Server
128.91.0.1
66.66.0.11
What kind of packets do you send to the victim?
Ideally, should be “connectionless”
  Difficult to spoof TCP connections
Should maximize the resources used by the victim
SYN
SYN

## Slide 43: TCP SYN Flood
TCP stack keeps track of connection state in data structures called Transmission Control Blocks (TCBs)
  New TCB allocated by the kernel whenever a listen socket receives a SYN
  TCB must persist for at least one RTO
Attack: flood the victim with SYN packets
  Exhaust available memory for TCBs, prevent legitimate clients from connecting
  Crash the server OS by overflowing kernel memory
Advantages for the attacker
  No connection – each SYN can be spoofed, no need to hear responses
  Asymmetry – attacker does not need to allocate TCBs

## Slide 44: Defending Against SYN Floods: SYN Cookies
Key idea: avoid storing TCB state on the server until after the three-way handshake is complete
What state in the TCB can be recovered from the client’s ACK?
  Source IP and port
  Destination IP and port
  Maximum Segment Size (MSS) for the connection
  Initial Acknowledgement Number from the source
  Initial Sequence Number (ISN)
SYN cookie construction
  Encode the MSS, a secret, and consistency check into the ISN in the SYN-ACK
  Verify the secret and consistency check when the ACK is returned
Trivially known by the server
Guaranteed to be in the ACK

## Slide 45: SYN Cookies
Maximum segment size (MSS)
  Stated by the client during initial SYN, must be “remembered” by the server
  Reflect the client’s value back through them
  Limitation: 8-bit MSS must be encoded in 3-bits
Validation: did the client really send me a SYN recently?
  Timestamp: freshness check, prevents replay attacks
  Cryptographic hash w/ secret key: prevents spoofed packets
Sequence Number
timestamp
31
0
5
MSS
8
hash(src_ip, src_port, timestamp, secret)
ISN:

## Slide 46: SYN Cookies in Practice
Advantages
  Effective at mitigating SYN floods
  Compatible with all TCP versions
  Only need to modify the server, no need for client support
Disadvantages
  MSS limited to 3 bits, may be smaller than clients actual MSS
  Server forgets all other TCP options included with the client’s SYN
    SACK support, window scaling, etc.

## Slide 47: Sources
Stress Testing the Booters: Understanding and Undermining the Business of DDoS Services -- https://dl.acm.org/citation.cfm?id=2883004
Taming the 800 Pound Gorilla: The Rise and Decline of NTP DDoS Attacks -- https://dl.acm.org/citation.cfm?id=2663717
Exit from Hell? Reducing the Impact of Amplification DDoS Attacks -- https://www.usenix.org/system/files/conference/usenixsecurity14/sec14-paper-kuhrer.pdf