## Slide 1: CS 4700 / CS 5700 Network Fundamentals
Lecture 21: Quality of Service
(Why is my ping time 1000ms!?!?)

## Slide 2: Motivation
Internet is designed to give best-effort service
  i.e. all packets are treated the same
However, not all packets are the same
  HTTP – delay sensitive
  Voice/Video streaming – delay and jitter sensitive
  Online Games – delay and jitter sensitive
  BitTorrent – totally insensitive
    Delay, jitter, bandwidth do not matter
    File transfer will finish eventually
Should the network give better quality to some packets?

## Slide 3: Three Relevant Factors
Application performance
  How much bandwidth do you need?
  What about delay and jitter?
Bandwidth required to provide performance
  How to meet performance goals…
  While still offering general service to all applications
Complexity/cost of required mechanisms
  How to modify the network to meet perf. goals?
  Political concerns, e.g. network neutrality
  Security

## Slide 4: QoS: Quality of Service
Idea: build some unfairness into the network
  Some traffic is high priority, gets better service
  Some traffic is low priority, gets reduced service
Thus, “important” traffic receives “better” service
  What traffic is important?
  What do we mean by “better” service?
    Is the gain guaranteed and strictly defined?
    Is the gain relative and fungible?

## Slide 5: Outline
“Soft” QoS
  Packet shaping/prioritization
  DiffServ
“Hard” QoS
  IntServ

## Slide 6: The Problem at the Edge
Problem: sharing resources between applications
Packet Queue
Large, long lived flows can dominate the queue
  Elephants vs. Mice

## Slide 7: Port-Based Priority Queues
Port-based QoS
  Very common in home routers
High Priority Queue (Port 22, 25, 80, 110)
Low Priority Queue (all other ports)

## Slide 8: QoS at Internet Scale
Priority queues at the edge of the network help
  … but what about QoS across the entire Internet?
Large area of research in the 1990’s
  Differentiated Service (DiffServ)
    Class-based traffic management mechanism
    Coarse grain control
    Relative performance improvements / lower overhead
  Integrated Service (IntServ)
    Flow-based traffic management mechanism
    Fine grained control
    Guaranteed performance / high overhead

## Slide 9: Differentiated Services (DiffServ)
Goal: offer different levels of service to packets
  Organized around domains (ASs)
  Involves edge and core routers (sometimes hosts too)
Edge routers
  Sort packets into classes (based on many factors)
  Set bits (DiffServ Code Point) in packet headers
  Police/shape traffic
Core Routers
  Handle per-hop packet behavior based on DSCP

## Slide 10: IP Header, Revisited
Version
HLen
DSCP/ECN
Datagram Length
0
8
16
24
31
4
12
19
Identifier
Flags
Offset
TTL
Protocol
Checksum
Source IP Address
Destination IP Address
Options (if any, usually not)
Data
DiffServ Code Point
Used to label the class of the packet

## Slide 11: DiffServ at a High-Level
AS-1
AS-2
Ingress/Egress routers assign class to each packet
  Must analyze each packet, high overhead
Core routers use classes to do priority queuing
Classes may switch between AS boundaries
Ingress/Egress Routers
Core
Routers

## Slide 12: Per-Hop Behavior
Traffic classes indicated by 6-bit DSCP in IP header
  In practice, only 3 classes used
Default PHB: best-effort forwarding
  Same as usual for the Internet
Expedited Forwarding (EF) PHB
  Traffic requiring low delay, low loss, low jitter
  Often given strict priority queuing above other classes
  Admission control limits to 30% of capacity
    Why?
Assured Forwarding (AF) PHB
  More general class with assurance of delivery
  Only if traffic rate < subscribed rate

## Slide 13: How do we Classify Packets?
It depends.
  Based on ports
    i.e. 80 (HTTP) takes precedence over 21 (FTP)
  Based on application
    i.e. HTTP takes precedence over BitTorrent
  Based on location
    i.e. home users get normal service…
    While hospitals/policy/fire department get priority service
  Based on who pays more $$$
    $100 for “premium” Internet vs. $25 “value” Internet

## Slide 14: Traffic Policing/Shaping
Purpose: need a mechanism to control packet flow
  High vs. medium vs. low priority flows
  Think of it like a toll booth
Token bucket (r, b)
  r  rate the bucket fills
  b  size of tokens in the bucket
Police: if token is available, packet may pass
  Otherwise, packet is queued or dropped
  Queuing packets “shapes” the traffic flow

## Slide 15: Leaky Buckets
Parameters
  r –rate at which tokens fill the bucket
  b – bucket depth
  R – maximum link capacity or peak rate
r bps
b bits
<= R bps
Bits are only transmitted from a queue when there is a token of sufficient size available
Packet Queue

## Slide 16: Bucket Parameters, Intuitively
r – speed packets can exit the queue
b – burst tolerance
Fast r
Slow r
Small b
Large b

## Slide 17: Advantages of DiffServ
Giving priority does improve performance
  … at the expense of reduced perf. for lower classes
Relatively lightweight solution
  Some overhead on ingress/egress routers
  No per flow state, low overhead on core routers
Easy to deploy
  No hard reservations
  No advanced setup of flows
  No end-to-end negotiation

## Slide 18: Disadvantages of DiffServ
No performance guarantees
  All gains are relative, not absolute
  Classes are very course
    i.e. all packets of a specific class get better performance
    No per flow or per destination QoS
  What if some ASs do not support DiffServ?
  Impossible to predict end-to-end behavior
Security
  Any host can tag traffic as high priority
  E.g. Win 2K tagged all traffic as high priority by default

## Slide 19: Outline
“Soft” QoS
  Packet shaping/prioritization
  DiffServ
“Hard” QoS
  IntServ

## Slide 20: From Relative to Absolute Service
Priority mechanisms can only deliver absolute assurances if total load is regulated
Service Level Agreements (SLAs) specify:
  Amount user (organization, etc.) can send
  Level of service delivered to that traffic
DiffServ offers low (but unspecified) delay and no drops
  Acceptance of proposed SLAs managed by “Bandwidth Broker”
  Only over long time scales

## Slide 21: Inter-Domain Premium DiffServ
Goal of IntServ: end-to-end bandwidth guarantees
Mechanism: end-to-end bandwidth reservations
  Like the telephone network, circuit reservations
  End hosts ask for reserved capacity from the network
AS-1
AS-2
Please reserve 1 Mbps
?
?
?
?
?
?
?

## Slide 22: Philosophical Battle
If your network allows reservations:
  Then you must perform admission control
  i.e. who can make reservations, and when?
Basic Question:
  Should all flows be admitted (current Internet)
  Or, should we refuse some flows to guarantee good service for reserved flows (IntServ Internet)
Which one is right?!?!

## Slide 23: High-Level IntServ Design
Reservations are made by endpoints
  Applications know their own requirements
  Applications run on end-hosts
  Network does not need to guess about requirements
Guarantees are end-to-end on a per-flow basis
Soft-state
  State in routers constantly refreshed by endpoints
IntServ is multicast-oriented
  Assumed that large broadcasts would drive multicast and IntServ deployment
  This is why reservations are made by receivers

## Slide 24: Requirements for IntServ
Fixed, stable paths
  Only routers on the path know about the reservation
  Current Internet cannot guarantee this
Routers maintain per-flow state
  Very high overhead (even with soft-state)
State is used to reserve bandwidth
  Guarantees QoS for reserved flows
  … but some flows may not be admitted
  Security?

## Slide 25: RSVP Reservation Protocol
Performs signaling to set up reservation state
  Initiated by the receiver
Each reservation is a simplex data flow sent to a unicast or multicast address
  <Destination IP, protocol # (TCP, UDP), port #>
Multiple senders/receivers can be in the same session

## Slide 26: RSVP Example
PATH
PATH
RESV
Soft-state: PATH and RESV need to be periodically refreshed

## Slide 27: IntServ Summary
The good:
  Reservations are guaranteed and precise
    Reserved bandwidth is not shared with a class
    Tight allocations for each flow
  Soft-state slightly reduces overhead on routers
The bad:
  IntServ is a whole Internet upgrade
  Heavyweight mechanisms, per flow state
  Security: end-hosts can DoS by reserving lots of bandwidth

## Slide 28: QoS on the Internet Today
QoS was huge in the ‘90s
  DiffServ and IntServ are both IETF standards
  … yet neither are widely deployed today
Internet capacity explosion
  Packets only drop when capacity is reached
  QoS is only useful if capacity is saturated
After the 2000s Internet boom…
  Huge glut of “dark” fiber capacity
  Lots of spare capacity = little need for QoS
Another technical solution killed by economics

## Slide 29: QoS is Controversial
Example: ISP sometimes drop or throttle BitTorrent
  Net neutrality: is it okay to favor one kind of traffic over another?
  Privacy: is it okay for ISPs to snoop on packets?
Counterargument: BitTorrent negatively impacts other customers
  Is it okay for your neighbors BitTorrent traffic to make your Skype calls sound choppy?
Slippery slope:
  Who decides which apps are favored?
  Is it okay to ban apps entirely?
  Is it okay to allow people to pay for higher priority?