## Slide 1: CS 4700 / CS 5700 Network Fundamentals
Lecture 10: Inter Domain Routing
(It’s all about the Money)
Revised 9/25/2013

## Slide 2: Network Layer, Control Plane
Function:
  Set up routes between networks
Key challenges:
  Implementing provider policies
  Creating stable paths
Application
Presentation
Session
Transport
Network
Data Link
Physical
BGP
RIP
OSPF
Control Plane
Data Plane

## Slide 3: Outline
BGP Basics
Stable Paths Problem
BGP in the Real World
Next-gen Routing: HLP

## Slide 4: ASs, Revisited
AS-1
AS-2
AS-3
Interior Routers
BGP Routers

## Slide 5: AS Numbers
Each AS identified by an ASN number
  16-bit values
  64512 – 65535 are reserved
Currently, there are > 20000 ASNs
  AT&T: 5074, 6341, 7018, …
  Sprint: 1239, 1240, 6211, 6242, …
  Northeastern: 156
  North America ASs  ftp://ftp.arin.net/info/asn.txt

## Slide 6: Inter-Domain Routing
Global connectivity is at stake!
  Thus, all ASs must use the same protocol
  Contrast with intra-domain routing
What are the requirements?
  Scalability
  Flexibility in choosing routes
    Cost
    Routing around failures
Question: link state or distance vector?
  Trick question: BGP is a path vector protocol

## Slide 7: BGP
Border Gateway Protocol
  De facto inter-domain protocol of the Internet
  Policy based routing protocol
  Uses a Bellman-Ford path vector protocol
Relatively simple protocol, but…
  Complex, manual configuration
  Entire world sees advertisements
    Errors can screw up traffic globally
  Policies driven by economics
    How much $$$ does it cost to route along a given path?
    Not by performance (e.g. shortest paths)

## Slide 8: BGP Relationships
Customer
Provider
Customer pays provider
Peer 1
Peer 2
Peer 3
Peers do not pay each other
Peer 2 has no incentive to route 1 3
Customer
Customer
Provider

## Slide 9: Tier-1 ISP Peering
AT&T
Centurylink
XO Communications
Inteliquent
Verizon Business
Sprint
Level 3

## Slide 11: Peering Wars
Reduce upstream costs
Improve end-to-end performance
May be the only way to connect to parts of the Internet
You would rather have customers
Peers are often competitors
Peering agreements require periodic renegotiation
Peer
Don’t Peer
Peering struggles in the ISP world are extremely contentions, agreements are usually confidential

## Slide 12: Two Types of BGP Neighbors
IGP
Exterior routers also speak IGP
eBGP
eBGP
iBGP
iBGP

## Slide 13: Full iBGP Meshes
Question: why do we need iBGP?
  OSPF does not include BGP policy info
  Prevents routing loops within the AS
iBGP updates do not trigger announcements
eBGP
iBGP

## Slide 14: Path Vector Protocol
AS-path: sequence of ASs a route traverses
  Like distance vector, plus additional information
Used for loop detection and to apply policy
Default choice: route with fewest # of ASs
110.10.0.0/16
AS 1
AS 2
130.10.0.0/16
AS 3
120.10.0.0/16
AS 4
AS 5
120.10.0.0/16: AS 2  AS 3  AS 4
130.10.0.0/16: AS 2  AS 3
110.10.0.0/16: AS 2  AS 5

## Slide 15: BGP Operations (Simplified)
Establish session on TCP port 179
Exchange active routes
Exchange incremental updates
AS-1
AS-2
BGP Session

## Slide 16: Four Types of BGP Messages
Open: Establish a peering session.
Keep Alive: Handshake at regular intervals.
Notification: Shuts down a peering session.
Update: Announce new routes or withdraw previously announced routes.
announcement = IP prefix + attributes values

## Slide 17: BGP Attributes
Attributes used to select “best” path
  LocalPREF
    Local preference policy to choose most preferred route
    Overrides default fewest AS behavior
  Multi-exit Discriminator (MED)
    Specifies path for external traffic destined for an internal network
    Chooses peering point for your network
  Import Rules
    What route advertisements do I accept?
  Export Rules
    Which routes do I forward to whom?

## Slide 18: Route Selection Summary
Highest Local Preference
Shortest AS Path
Lowest MED
Lowest IGP Cost to BGP Egress
Lowest Router ID
Traffic engineering
Enforce relationships
When all else fails,
break ties

## Slide 19: Shortest AS Path != Shortest Path
Source
Destination
?
?
4 hops
4 ASs
9 hops
2 ASs

## Slide 20: Hot Potato Routing
Destination
Source
3 hops total,
3 hops cost
?
?
5 hops total, 2 hops cost

## Slide 21: Importing Routes
From Provider
From Peer
From Peer
From Customer
ISP Routes

## Slide 22: Exporting Routes
To Customer
To Peer
To Peer
To Provider
Customers get all routes
Customer and ISP routes only
$$$ generating routes

## Slide 23: Outline
BGP Basics
Stable Paths Problem
BGP in the Real World
Next-gen Routing: HLP

## Slide 24: What Problem is BGP Solving?
Underlying Problem | Distributed Solution
Shortest Paths | RIP, OSPF, IS-IS, etc.
??? | BGP
Knowing ??? can:
  Aid in the analysis of BGP policy
  Aid in the design of BGP extensions
  Help explain BGP routing anomalies
  Give us a deeper understanding of the protocol

## Slide 25: The Stable Paths Problem
An instance of the SPP:
  Graph of nodes and edges
  Node 0, called the origin
  A set of permitted paths from each node to the origin
    Each set contains the null path
  Each set of paths is ranked
    Null path is always least preferred
2
0
1
2
4
3
5
2 1 0
2 0
5 2 1 0
4 2 0
4 3 0
3 0
1 3 0
1 0

## Slide 26: A Solution to the SPP
A solution is an assignment of permitted paths to each node such that:
  Node u’s path is either null or uwP, where path uw is assigned to node w and edge u  w exists
  Each node is assigned the higest ranked path that is consistent with their neighbors
2
0
1
2
4
3
5
2 1 0
2 0
5 2 1 0
4 2 0
4 3 0
3 0
1 3 0
1 0
Solutions need not use the shortest paths, or form a spanning tree

## Slide 27: Simple SPP Example
2
0
1
2
4
3
1 0
1 3 0
2 0
2 1 0
3 0
4 2 0
4 3 0
4 3 0
4 2 0
Each node gets its preferred route
Totally stable topology

## Slide 28: Good Gadget
2
0
1
2
4
3
1 3 0
1 0
2 1 0
2 0
3 0
4 3 0
4 2 0
Not every node gets preferred route
Topology is still stable
Only one stable configuration
  No matter which router chooses first!

## Slide 29: SPP May Have Multiple Solutions
0
1
2
1 2 0
1 0
2 1 0
2 0
0
1
2
1 2 0
1 0
2 1 0
2 0
0
1
2
1 2 0
1 0
2 1 0
2 0

## Slide 30: Bad Gadget
2
0
1
2
4
3
1 3 0
1 0
2 1 0
2 0
3 4 2 0
3 0
4 2 0
4 3 0
That was only one round of oscillation!
This keeps going, infinitely
Problem stems from:
  Local (not global) decisions
  Ability of one node to improve its path selection

## Slide 31: SPP Explains BGP Divergence
BGP is not guaranteed to converge to stable routing
  Policy inconsistencies may lead to “livelock”
  Protocol oscillation
Must
Converge
Must
Diverge
Solvable
Can Diverge
Good Gadgets
Bad Gadgets
Naughty Gadgets

## Slide 32: Beware of Backup Policies
2
0
1
2
4
3
1 3 0
1 0
2 1 0
2 0
3 4 2 0
3 0
4 0
4 2 0
4 3 0
BGP is not robust
It may not recover from link failure

## Slide 33: BGP is Precarious
6
3
4
5
3 1 0
3 1 2 0
5 3 1 0
5 6 3 1 2 0
5 3 1 2 0
0
1
2
1 2 0
1 0
2 1 0
2 0
4 3 1 0
4 5 3 1 2 0
4 3 1 2 0
6 3 1 0
6 4 3 1 2 0
6 3 1 2 0
If node 1 uses path 1  0, this is solvable
No longer stable

## Slide 34: Can BGP Be Fixed?
Unfortunately, SPP is NP-complete
Static Approach
Inter-AS
coordination
Automated Analysis
of Routing Policies
(This is very hard)
Dynamic Approach
Extend BGP to
detecting and suppress
policy-based oscillations?
These approaches are complementary
Possible Solutions

## Slide 35: Outline
BGP Basics
Stable Paths Problem
BGP in the Real World
Next-gen Routing: HLP

## Slide 36: Motivation
Routing reliability/fault-tolerance on small time scales (minutes) not previously a priority
Transaction oriented and interactive applications (e.g. Internet Telephony) will require higher levels of end-to-end network reliability
How well does the Internet routing infrastructure tolerate faults?
Notes: Motivation  why we should care about convergence

## Slide 37: Conventional Wisdom
Internet routing is robust under faults
  Supports path re-routing
  Path restoration on the order of seconds
BGP has good convergence properties
  Does not exhibit looping/bouncing problems of RIP
Internet fail-over will improve with faster routers and faster links
More redundant connections (multi-homing) will always improve fault-tolerance

## Slide 38: Delayed Routing Convergence
Conventional wisdom about routing convergence is not accurate
  Measurement of BGP convergence in the Internet
  Analysis/intuition behind delayed BGP routing convergence
  Modifications to BGP implementations which would improve convergence times

## Slide 39: Open Question
After a fault in a path to multi-homed site, how long does it take for majority of Internet routers to fail-over to secondary path?
Customer
Primary ISP
Backup ISP
Route Withdrawn
Traffic
Routing table convergence
Stable end-to-end paths

## Slide 40: Bad News
With unconstrained policies:
  Divergence
  Possible create unsatisfiable policies
  NP-complete to identify these policies
  Happening today?
With constrained policies (e.g. shortest path first)
  Transient oscillations
  BGP usually converges
  It may take a very long time…
This paper is about constrained policies

## Slide 41: 16 Month Study of Convergence
Instrument the Internet
  Inject BGP faults (announcements/withdrawals) of varied prefix and AS path length into topologically and geographically diverse ISP peering sessions
  Monitor impact faults through
    Recording BGP peering sessions with 20 tier1/tier2 ISPs
    Active ICMP measurements (512 byte/second to 100 random web sites)
  Wait two years (and 250,000 faults)

## Slide 42: Measurement Architecture
Researchers pretending to be an AS
Researchers pretending to be an AS

## Slide 43: Announcement Scenarios
Tup – a new route is advertised
Tdown – A route is withdrawn
  i.e. single-homed failure
Tshort – Advertise a shorter/better AS path
  i.e. primary path repaired
Tlong – Advertise a longer/worse AS path
  i.e. primary path fails

## Slide 44: Major Convergence Results
Routing convergence requires an order of magnitude longer than expected
  10s of minutes
Routes converge more quickly following Tup/Repair than Tdown/Failure events
  Bad news travels more slowly
Withdrawals (Tdown) generate several more announcements than new routes (Tup)

## Slide 45: Example
BGP log of updates from AS2117 for route via AS2129
One withdrawal triggers 6 announcements and one withdrawal from 2117
Increasing AS path length until final withdrawal

## Slide 46: Why So Many Announcements?
Route Fails: AS 2129
Announce: 5696 2129
Announce: 1 5696 2129
Announce: 2041 3508 2129
Announce: 1 2041 3508 2129
Route Withdrawn: 2129
AS 2129
AS 5696
AS 1
AS 2117
AS 2041
AS 3508
Events from AS 2177

## Slide 47: How Many Announcements Does it Take For an AS to Withdraw a Route?
Answer: up to 19

## Slide 48
Short->Long Fail-Over
New Route
Long->Short Fail-over
Failure
Less than half of Tdown events converge within two minutes
Tup/Tshort and Tdown/Tlong form equivalence classes
Long tailed distribution (up to 15 minutes)
BGP Routing Table Convergence Times

## Slide 49: Failures, Fail-overs and Repairs
Bad news does not travel fast…
Repairs (Tup) exhibit similar convergence as long-short AS path fail-over
Failures (Tdown) and short-long fail-overs (e.g. primary to secondary path) also similar
  Slower than Tup (e.g. a repair)
  80% take longer than two minutes
  Fail-over times degrade the greater the degree of multi-homing

## Slide 50: Intuition for Delayed Convergence
There exists possible ordering of messages such that BGP will explore ALL possible AS paths of ALL possible lengths
BGP is O(N!), where N number of default-free BGP routers in a complete graph with default policy

## Slide 51: Impact of Delayed Convergence
Why do we care about routing table convergence?
  It deleteriously impacts end-to-end Internet paths
ICMP experiment results
  Loss of connectivity, packet loss, latency, and packet re-ordering for an average of 3-5 minutes after a fault
Why?
  Routers drop packets when next hop is unknown
  Path switching spikes latency/delay
  Multi-pathing causes reordering

## Slide 52: In real life …
Discussed worst case BGP behavior
In practice, BGP policy prevents worst case from happening
BGP timers also provide synchronization and limits possible orderings of messages

## Slide 53: Outline
BGP Basics
Stable Paths Problem
BGP in the Real World
Next-gen Routing: HLP

## Slide 54: Inter-Domain Routing
BGP4 is the only inter-domain routing protocol currently in use world-wide
Issues?
  Lack of security
  Ease of misconfiguration
  Poorly understood interaction between local policies
  Poor convergence
  Lack of appropriate information hiding
  Non-determinism
  Poor overload behavior

## Slide 55: Policy, policy, and policy
An ISP’s routing policy is a commercial secret
  Don’t want to tell anyone else what the policy is
  BGP does policy entirely through local filtering of the set of possible alternative routes
However, you need path information to set a useful range of policies
  But path information inherently reveals information about routing adjacencies…

## Slide 56: Does Policy Hiding Even Work?
It is practical to hide many private peering relationships
It’s not practical to hide most customer/provider routing relationships when using BGP
  Customer pays provider to advertise their route to the rest of the world
95% of the “peerings” visible in route-views and RIPE appear to function as customer/provider links
  Note that the flow of $ is not revealed by routing protocols

## Slide 57: Problems with Local Filtering
Doing policy entirely through local filtering is the root cause of many of BGP’s problems
Manual configuration of what not to accept  prone to misconfiguration
No semantics describing why a route is used  hard to discover errors or attacks
No information about alternative routes  BGP must do a lengthy path exploration to find feasible alternatives
No information about which alternatives will work for whom  BGP can’t do effective information hiding
  Small changes in one part of the world are frequently globally visible

## Slide 58: Towards a New Routing Framework
Given that:
  Most links function as customer/provider
  Customer/provider links are inherently visible to the world
Additional semantics visible in the routing protocol would allow:
  More informed route calculation
  Permit better information hiding
Thus, it seems logical to design a routing protocol that uses this information explicitly

## Slide 59: Routing Hierarchy
Customer / Provider Links
Peering Links
Customer / Provider Hierarchy

## Slide 60: Multiple Routing Hierarchies
Within the hierarchy:
  No need to hide policy information
  More information  easier to make robust routing decisions
Peer relationships:
  Want to hide policy information
  No need to export low-level path changes
Use different routing protocols for inside and outside the hierarchy!

## Slide 61: Routing Protocol Styles
E.g. OSPF
Great convergence properties
Scales fairly well
Can’t easily hide policy information
E.g. BGP
Poor convergence properties
Scales well
Can hide policy information
Link State
Path Vector
Inside the Hierarchy (Customer / Provider Links)
Outside the Hierarchy
(Peering Links)

## Slide 62: Hybrid Link State/Path Vector (HLP)
Path Vector
Link State
Path Vector
Link State
Link State

## Slide 63: Link State HLP
Within customer/provider link state tree:
  Good convergence
  More information
    e.g. alternative route pre-computation
    Explicit representation of backup links for multi-homing
  Default policy is simple and robust
    Reduces misconfiguration errors
  Improved default security
    Need to be a tier-1 provider to do much damage

## Slide 64: Path Vector HLP
Between customer/provider trees (peering links):
  Use fragmented path-vector (FPV), rather than full path-vector used by BGP
    Number of links routed using FPV decreased drastically
    Reduces path-exploration space
  Degrade gracefully from link-state towards path-vector if ISPs need to use more non-default policies
    Worst case looks pretty much like BGP

## Slide 65: New Route Announcements
C
D
E
F
G
H
A
B
LSA: CE
Cost = 1
LSA: CE
Cost = 1
LSA: CE
Cost = 1
LSA: CE
Cost = 1
LSA: CE
Cost = 1
FPV: AE
Cost = 2
FPV: BAE
Cost = 3
FPV: BAE
Cost = 4

## Slide 66: Route Withdrawl
C
D
E
F
G
H
A
B
LSA: CE
Cost = ∞
LSA: CE
Cost = ∞
LSA: CE
Cost = ∞
LSA: CE
Cost = ∞
FPV: AE
Cost = 3
FPV: BAE
Cost = 4
FPV: BAE
Cost = 5

## Slide 67: Isolation and Information Hiding
Lots of information within a Customer-Provider tree
Don’t need to convey all changes into FPV
  Local changes that aren’t too critical can be hidden from the wider world
  Only large-scale changes need to be pushed via FPV
Significantly reduce global routing table churn

## Slide 68: Exceptions
Not all policies conform strictly to the hierarchy
  Export-policy exception
  Prefer-customer exception
Dealt with in HLP by using FPV rather than Link-state
Fortunately this is rare
Frequency of export-policy exceptions:

## Slide 69: Performance: Routing Table Churn
Churn: # of updates generated by single event

## Slide 70: Performance: Fault isolation
Isolation: # of AS’s affected by a single event

## Slide 71: Fault Isolation and Multihoming
Ratio of BGP to HLP isolation improvement

## Slide 72: Convergence
BGP: Worst case is fully connected n-node graph:
  Convergence time is O((n-1)!)
HLP: In the absence of exceptions, worst case is:
  Convergence time is O(nk(D))
  k(D) is number of peering links on path to D
In the current Internet:
  k ≤ 1 for 90% of Internet routes
  k ≤ 2 for 99% of Internet routes
  k ≤ 4 for all Internet routes

## Slide 73: HLP Advantages
Scalability: route churn is the issue
  Information hiding
  Separation of prefix distribution from routing
Convergence:
  Link-State converges fast
  FPV converges faster than Path-Vector because there are fewer infeasible alternates
Security:
  Structure adds security
  Secure prefix distribution separately from dynamic routing
Robustness:
  Harder to misconfigure, easier to figure out the intent behind a route

## Slide 74: HLP Summary
A really nice paper
  Great execution from a number of perspectives
Detailed need-driven system design
  Identify and isolate fundamental issues and tradeoffs: isolation versus reachability
  Decouple conflicting policies
  Sheds light on inner workings of complex system
Extremely well-written paper
  Clear logical reasoning
  Exceptional introduction
  Complete: from high-level design to protocol analysis to router implementation and microbenchmarks